## Slide 1: Bi/BE 177: Principles of Modern Microscopy
Lecture 02: Geometrical Optics
Andres Collazo, Director Biological Imaging Facility
Ke Ding, Graduate Student, TA
Wan-Rong (Sandy) Wong, Graduate Student, TA

## Slide 2: Lecture 2: Geometrical Optics
Speed of light and refractive index
Thin lens law
Simple optical system
Compound microscope I
Refractive indices and super lenses

## Slide 3: Simple microscope
How does it magnify?
By how much does it magnify?
Will the image be upright?
Why can’t this work for mag>100?
Why does the image have color halos?
Notes: Magnification ?
Right side up or upside down?
Why is metal creating pupil?

## Slide 4: The speed of light
299,792,458 metres per second in a vacuum
The meter is now defined by the speed of light (1983)
First measured by the Danish Astronomer Ole Rømer in 1676
James Clerk Maxwell proposed all electromagnetic waves move at the speed of light (1865)
Ole Rømer
James Clerk Maxwell
Notes: BBC: Albert Einstein has been voted the greatest physicist of all time in an end of the millennium poll, pushing Sir Isaac Newton into second place. Maxwell 3rd. The survey was conducted among 100 of today's leading physicists.

## Slide 5: How did we learn that the speed of light was finite?

## Slide 6: How did we learn that the speed of light was finite?
Hint

## Slide 7: How did we learn that the speed of light was finite?
Hint
Ole Rømer in 1676
Notes: Looked at orbit of Io around Jupiter. Io just discovered by Galileo in 1610. Io orbits at a good plane from earth so that it is eclipsed by Jupiter.

## Slide 8: Let’s review some of the concepts from last lecture
Simple vs.
Compound microscopes
Refraction
Notes: Discussed why we use visible light and its being perfect for analysis via geometrical optics.

## Slide 9
For most of today, will ignore the wave nature and concentrate on the particle nature.
Define the index of refraction, h
h = speed of light in vacuum /speed in medium
h = l in vacuum / l in medium
c = ν λ
Notes: Frequency does not change with medium.

## Slide 10
Medium Refractive Index
Air 1.0003
Water 1.33
Glycerin 1.47
Immersion Oil 1.518
Glass 1.56 – 1.46
Diamond 2.42
Refractive index η
Velocity in medium
299203
225032
203600
197162
191854 - 204995
123675

## Slide 11
Material Blue (486nm) Yellow (589nm) Red (656nm)
Crown Glass 1.524 1.517 1.515
Flint Glass 1.639 1.627 1.622
Water 1.337 1.333 1.331
Cargille Oil 1.530 1.520 1.516
COMPLICATION: h Depends on the wavelength
(more on this next lecture)

## Slide 12
Refraction - the bending of light as it passes from one material to another.
Snell’s Law: h1 sin q1 = h2 sin q2
h1
q1
q2
h2
Optical axis
Normal (perpendicular to interface of different materials)

## Slide 13
n1
1
2
n2
n1
??
Light beam through a plane-parallel glass plate
Snell’s Law: h1 sin q1 = h2 sin q2

## Slide 14
n1
1
2
n2
n1
1
Light beam through a plane-parallel glass plate
Snell’s Law: h1 sin q1 = h2 sin q2

## Slide 15: Geometrical optics: Light as collection of rays
n1
1
2
n2
n1
1
Refraction: light bends as it passes from one material to another
Snell’s Law: h1 sin q1 = h2 sin q2

## Slide 16
Could apply Snell’s Law to something as complex as a lens
h1 sin q1 = h2 sin q2 = h3 sin q3 = ….
h1
h2

## Slide 17
Thin lens laws
1. Ray through center of lens is straight

## Slide 18
Thin lens law 2
2. Light rays that enter the lens parallel to the optical axis leaves through Focal Point
Focal
Point
Notes: CONVERGENCE LENS. Convex lens

## Slide 19
Convex (biconvex) lens
This is a converging lens
Focal
Point
Notes: CONVERGENCE LENS. Convex lens

## Slide 20
Thin lens law 3
3. Light rays that enter the lens from the focal point exit parallel to the optical axis.
Focal
Point
f

## Slide 21: Using the thin lens laws to predict the behavior of imaging systems (principle ray technique)
f
f
Mark Focal Pt

## Slide 22: Applying thin lens law to our object, a gold can

## Slide 23
Ray through center of lens is straight

## Slide 24
Ray through center of lens is straight
Light rays that enter the lens parallel to the optical axis leaves through Focal Point

## Slide 25
Ray through center of lens is straight
Light rays that enter the lens parallel to the optical axis leaves through Focal Point
Light rays that enter the lens from the focal point, exit parallel to the optical axis.

## Slide 26
Where the three lines intersect is where that point of the object is located
Notes: Note that the object is magnified and inverted. Real Image.

## Slide 27
Ray tracing convention for optics generally uses arrows to represent the object.
Notes: Note that the object is magnified and inverted. Real Image.

## Slide 28
Same three rules can be applied for each point along the object.

## Slide 29
f
o
i
Thin Lens Equation
1/f = 1/o + 1/i

## Slide 30
f
o
i
Thin Lens Equation
1/f = 1/o + 1/i
Magnification = i/o

## Slide 31
f
o
i
Thin Lens Equation
1/f = 1/o + 1/i
Magnification = i/o
i =
i =
i = 75
Notes: Michel van Biezen’s lectures on youtube

## Slide 32
For object directly on focal point, rays focused to infinity.
Where would this be useful?

i =
Notes: Object located at greater than 2 x the focal distance result in small image. How cameras work.

## Slide 33
For object within the focal point, a virtual image is created.
Only need two rays to locate object.
i =
Notes: Virtual images are located on side of lens opposite to viewer. Bad naming conventions as virtual images are as “real” as a real image.

## Slide 34
Of course can use all three rules to trace three rays.

## Slide 35
So why can’t a simple lens magnify more than ~ 100X?

## Slide 36: What happens when you are at 2 x focal length?

## Slide 37: What happens when you are at 2 x focal length?
i =

## Slide 38: What happens when you are greater than 2 x focal length? Think of a camera

## Slide 39: What happens when you are greater than 2 x focal length? Think of a camera
i =

## Slide 40
Thin lens law (Concave Lenses)
Concave (biconcave) lens
This is a diverging lens
Notes: CONVERGENCE LENS. Convex lens

## Slide 41
Thin lens law (Concave Lenses)
Light rays that enter the lens parallel to the optical axis exit as if they came from the focal point on the opposite side.
Notes: CONVERGENCE LENS. Convex lens

## Slide 42
Thin lens law (Concave Lenses)
Focal length is defined as negative
Images are virtual
Notes: CONVERGENCE LENS. Convex lens

## Slide 43
Same three rules can be applied to a concave lens.
Notes: All concave lenses make virtual images that are smaller no matter where the object is located.
DISPERSION LENS

## Slide 44
But again two rays are enough to locate virtual image.
i =

## Slide 45
Concave lens makes virtual image that is smaller no matter where object is located****.
Notes: All concave lenses make virtual images that are smaller unless the object is located to the right of the lens. Only possible with multiple lenses.

## Slide 46
Principle ray approach works for complex lens assemblies.
Notes: Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn - Remember: for concave lens f is negative
Problem: Two thin lenses together don’t make a thin lens. Notice that the central ray misses the image.
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens.

## Slide 47
Principle ray approach works for complex lens assemblies.
Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn Remember: for concave lens f is negative
Notes: Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn - Remember: for concave lens f is negative
Problem: Two thin lenses together don’t make a thin lens. Notice that the central ray misses the image.
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens.

## Slide 48
Problem: Two thin lenses together don’t make a thin lens.
Notice that the central ray misses the image
Notes: Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn - Remember: for concave lens f is negative
Problem: Two thin lenses together don’t make a thin lens. Notice that the central ray misses the image.
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens.

## Slide 49
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens
Notice that the central ray misses the image
i =
Notes: Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn - Remember: for concave lens f is negative
Problem: Two thin lenses together don’t make a thin lens. Notice that the central ray misses the image.
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens.

## Slide 50
To avoid reciprocals: Define Diopter (D)
D = 1/focal length (in meters)
D(total) = D1 + D2 + ... + Dn Remember: for concave lens D is negative
Notes: Focal lengths add as reciprocals:
1/f(total) = 1/f1 + 1/f2 + ... + 1/fn - Remember: for concave lens f is negative
Problem: Two thin lenses together don’t make a thin lens. Notice that the central ray misses the image.
Solution: Use principle rays to define image from first lens. Then use the first image as the object for the second lens.

## Slide 51: Image in the eye are different sizes (different magnifications) depending on their distance from the eye. Accommodation of the lens changes f to make it possible.
MB ~ 2x MA
A
B

## Slide 52: Conventional Viewing Distance
250 mm
1x
?

## Slide 53
Solution: Add a “loupe” in front of eye
Allow eye to focus at infinity for o ≤ 250mm
Could get a larger retinal image if object were closer
Limited accommodation (especially with age)
Limited range
Notes: Focal length of eye is approximately 17 mm

## Slide 54: “Magnification” 1x
f = 250 mm
1x
1x

## Slide 55: Magnification via Single Lens
f = 250 mm
1x
Example: f=50mm
5x
Magnifying Glass (Loupe)
Notes: Why can’t this work for mag>100? Lens gets more spherical and closer to focal point.

## Slide 56: Magnification??
Delft
Imaging Path
Eyepiece
TubeLens
Objective
Condenser
Collector
Eye
Field Diaphragm
Specimen
Intermediate Image
Retina
Notes: The Leewenhoek microscope was simplicity in itself. It had a single lens mounted on a metal plate with screws to move the specimen across the field of view and to focus its image. The lens was the key and permitted magnification of 70 to 270. (web site seems incorrect on magnification range)
http://www.asu.edu/courses/phs208/patternsbb/PiN/rdg/elmicr/optical.shtml

## Slide 57
How to get magnification > 100??
Compound microscope
  Objective lens (next to the object)
Image
Objective Lens
Real image
Magnification = I/O
I=160mm (old microscopes)

## Slide 58
How to get magnification > 100??
Compound microscope
Objective lens (next to the object)
Eyepiece (f = 25mm; 10x)
Reticle position
(in focus for eye)
Note rays are parallel

## Slide 59
How to get magnification > 100??
Compound microscope
Objective lens (next to the object)
Eyepiece (f = 25mm; 10x)
Image
Objective Lens
Eyepiece
image
Eyepiece
Lens of eye

## Slide 60
How to get magnification > 100??
Compound microscope
Objective lens (next to the object)
Eyepiece (f = 25mm; 10x)
Image
Objective Lens
Eyepiece
image
Eyepiece
Lens of eye

## Slide 61
Intermediate Image
Eyepoint (Exit Pupil)
The Eyepiece (Ocular)
Note: If you need a magnifier, turn eyepiece
upside down and move close to eye

## Slide 62
Intermediate Image
Eyepoint (Exit Pupil)
The Eyepiece (Ocular)
Question: why does the eye need to be at the focus of the eyepiece?

## Slide 63: Eye at focal point because…
…it maximizes field of view.

## Slide 64
Object viewed through microscope vs the unaided eye
(250 mm from eye)
1x view
Small image on retina
Compound microscope
Large image on retina

## Slide 65
Homework 1: The index of refraction changes with wavelength (index is larger in blue than red).
How would you need to modify this diagram of the rays of red light to make it appropriate for blue light?
f
o
i
Hint: higher index of refraction results in shorter f

## Slide 66: Let’s come back to refractive index (η)
Material | Refractive Index
Air | 1.0003
Water | 1.33
Glycerin | 1.47
Immersion Oil | 1.515
Glass | 1.52
Diamond | 2.42
η = speed of light in vacuum /speed in medium
Notes: What do you notice about the values?

## Slide 67: Metamaterials with negative refractive indices would produce bizarre images
Image not real!
Tyc T, Zhang X (2011) Forum Optics: Perfect lenses in focus. Nature 480: 42-43.
Notes: http://www.nature.com/nature/journal/v480/n7375/full/480042a.html
Straw image from http://www.extremetech.com/extreme/168060-the-first-quantum-metamaterial-raises-more-questions-than-it-answers

## Slide 68: Metamaterials with negative refractive indices could be used to make superlenses for super resolution microcopy
Do you need perfect lens?
Maxwell's fish-eye lens could do it with positive refractive indices
  Refractive index changes across lens (blue shading)
Luneburg lens
Tyc T, Zhang X (2011) Forum Optics: Perfect lenses in focus. Nature 480: 42-43.
Notes: Darker blue, higher refractive index. Like a gravitational lens
A practical superlens, super lens or perfect lens, is a lens which uses metamaterials to go beyond the diffraction limit. The diffraction limit is an inherent limitation in conventional optical devices or lenses.[1] In nano-optics, a plasmonic lens generally refers to a lens for surface plasmon polaritons (SPPs), i.e. a device that redirects SPPs to converge towards a single focal point. Since SPPs can have very small wavelength, they can converge into a very small and very intense spot, much smaller than the free-space wavelength and the diffraction limit.[1][2] Surface plasmon polaritons (SPPs), are infrared or visible-frequency electromagnetic waves, which travel along a metal-dielectric or metal-air interface. The term "surface plasmon polariton" explains that the wave involves both charge motion in the metal ("surface plasmon") and electromagnetic waves in the air or dielectric ("polariton").[1]
They are a type of surface wave, guided along the interface in much the same way that light can be guided by an optical fiber. SPPs are shorter in wavelength than the incident light (photons).[2]
Metamaterials are artificial materials engineered to have properties that have not yet been found in nature.