## Slide 1: Bi/BE 177: Principles of Modern Microscopy
Lecture 13: Single Molecule Imaging
Andres Collazo, Director Biological Imaging Facility
Ke Ding, Graduate Student, TA
Wan-Rong (Sandy) Wong, Graduate Student, TA

## Slide 2: Lecture 13: Single molecule imaging
Overview of approaches
Fluorescence fluctuation spectroscopy (FFS)
  Fluorescence correlation spectroscopy (FCS)
    Some concrete examples of what we can learn
  Fluorescence cross correlation spectroscopy (FCCS)
  Photon counting histogram (PCH)
FRAP/FLIP

## Slide 3: Questions about last lecture?

## Slide 4: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?

## Slide 5: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?
Tracking single molecules using light microscopy

## Slide 6: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?
Tracking single molecules using light microscopy
  Following the same molecule over time
  Discerning behavior of single molecules from a population

## Slide 7: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?
Tracking single molecules using light microscopy
  Following the same molecule over time
  Discerning behavior of single molecules from a population
Problems?
Notes: Density

## Slide 8: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?
Tracking single molecules using light microscopy
  Following the same molecule over time
  Discerning behavior of single molecules from a population
Problems?

## Slide 9: Tracking single molecules using light microscopy
Following the same molecule over time

## Slide 10: Tracking single molecules using light microscopy
Following the same molecule over time
Use EMCCD or sCMOS camera?
  Electron multiplication (Cascade) CCD
  Scientific CMOS
Notes: http://meroli.web.cern.ch/lecture_cmos_vs_ccd_pixel_sensor.html

## Slide 11: Single molecule imaging
Detection versus Resolving
  Can’t resolve but can detect
Applications?
Tracking single molecules using light microscopy
  Following the same molecule over time
  Discerning behavior of single molecules from a population
Problems?

## Slide 12: The “F” words
FRET
FRAP
FLIM
FCCS
FCS
FFS
FACS
FIGS
FLAM
Notes: FACS (fluorescence-activated cell sorting). One of several important cell sorting techniques used in the separation of different cell lines (especially those isolated from animal tissues).
FIGS (Fluorescence image-guided surgery) is a medical imaging technique that uses fluorescence to detect properly labeled structures during surgery.

## Slide 13: The “F” words
FRET
FRAP
FLIM
FCCS
FCS
FFS
FACS
FIGS
FLAM
Notes: FACS (fluorescence-activated cell sorting). One of several important cell sorting techniques used in the separation of different cell lines (especially those isolated from animal tissues).
FIGS (Fluorescence image-guided surgery) is a medical imaging technique that uses fluorescence to detect properly labeled structures during surgery.

## Slide 14: Fluorescence correlation spectroscopy (FCS)
In 1972 Watt Webb’s laboratory at Cornell put fluorescence microscopy to new use
Studied reaction kinetics
Ethidium bromide binding to DNA
  Individually don’t fluoresce but together glow under UV
Could detect single molecules but could not repeatedly detect the same molecule
Notes: http://www.nature.com/milestones/milelight/full/milelight10.html
1990 invented two photon confocal microscopy

## Slide 15: Fluorescence Fluctuation Spectroscopy (FFS)
Fluorescence Correlation Spectroscopy (FCS)
Photon Counting Histogram (PCH)
Fluorescence Cross-Correlation Spectroscopy (FCCS)
  FCS with more than 1 color

## Slide 16: Fluorescence Fluctuation Spectroscopy (FFS)
Causes of fluctuations
Diffusion of labeled molecules due to Brownian motion
  In cells wide range of things cause movement (cellular trafficking, protein interaction etc.)
Photophysical processes of labeled molecules

## Slide 17: Fluorescence Fluctuation Spectroscopy (FFS)
Advantages over FRAP and FRET
Table: http://www.fcsxpert.com/

## Slide 18: Fluctuations Carry the Information
Measured intensity fluctuations reflects (mobile fraction only)
  Number of particles
    concentration
  Diffusion of particles
    interaction
  Brightness
    Oligomerization
A particle that transits the confocal volume will generate groups of pulses.
  The correlation function calculates the mean duration time t of these groups.
  The variance/histogram of the signal yields information about oligomeric state
<I(t)>
dI(t)
dI(t)
FCS
PCH
Notes: The principle of FCS is being able to observe one or a few fluorescent particles enter and leave a small illuminated volume. If the sample, solution or cell, has a high concentration of tagged molecules it becomes hard to observe the needed fluctuations. I generally give the analogy of a crowded lecture hall. If the lecture hall is crowded and you were observing the lecture hall you would be less apt to notice if some one entered or left the room (i.e. a small fluctuation from the mean number of people in the hall). If only a few people were in the hall, then if someone left it would be very easy to notice (i.e. a large fluctuation from the mean number of people in the hall). This is why a large immobile population is not good for FCS. Fluctuations about the mean intensity is the information used for all FFS techniques.

## Slide 19: Fluorescence Fluctuation Spectroscopy (FFS)
Bacia et al., Nature Methods 2006
Notes: Bacia, K., Kim, S.A., Schwille, P., 2006. Fluorescence cross-correlation spectroscopy in living cells. Nat Methods 3, 83-89.

## Slide 20: Fluorescence Fluctuation Spectroscopy (FFS)
Bacia et al., Nature Methods 2006
wr2
4td,i
D=
Diffusion coefficient:
Notes: Bacia, K., Kim, S.A., Schwille, P., 2006. Fluorescence cross-correlation spectroscopy in living cells. Nat Methods 3, 83-89.

## Slide 21: Creating the Autocorrelation Function
“Copy” signal
Photon Burst
dI(t)
dI(t+t)
t=0
t=tD
t=inf
Notes: The fluctuations generated can be analyzed in many ways. FCS relies on the auto-correlation function which is a signal processing technique. The autocorrelation compares a signal against itself. In this case, a particle enters the focal volume and generates a photon burst. The collected signal is “copied” and the two copies are compared against one another as you shift the “copy” in time. The copy signal is shifted by some amount of time given by the greek symbol tau. All data analysis will be done in reference to the shift time tau.

## Slide 22: FCS Correlation Function
The correlation function
CF G(t)
amplitude: number of molecules
Decay time: diffusion time
offset: very slow processes

## Slide 23: Autocorrelation Function
kQ = quantum yield and detector sensitivity (how bright is our probe). This term could contain the fluctuation of the fluorescence intensity due to internal processes
W(r) describes our
observation volume
C(r,t) is a function of the fluorophore concentration over time. This is the term that contains the “physics” of the diffusion processes
Factors influencing the fluorescence signal:
Notes: Lecture 5 FCS, Autocorrelation, PCH, Cross-correlation Enrico Gratton

## Slide 24: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 25: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 26: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 27: Independent Processes Contribute Fluctuations
Contributions of single independent processes multiply
More process system
1E-6
1E-5
1E-4
1E-3
0.01
0.1
1
10
100
1000
10000
1.0
1.1
1.2
1.3
1.4
1.5
G(
t
)
t
[ms]
diffusion
triplet
exponential

## Slide 28: Additional Equations for these independent processes:
... where N is the average particle number, tD is the diffusion time (related to D, tD=w2/8D, for two photon and tD=w2/4D for 1-photon excitation), and S is a shape parameter, equivalent to w/z in the previous equations.
3D Gaussian Confocor analysis:
Triplet state term:
..where T is the triplet state amplitude and tT is the triplet lifetime.

## Slide 29
4nsec
Add in Interstate Crossing (ISC)
0.8 emitted
fluorescence
ISC
~0.03
Excited triplet
state
Phosphorescence
(usec - msec)
Triplet state is long lived.
Therefore even low probability can deplete active dye
(steady state reached in ~200msec
~80-90% in triplet --> 5-10 fold dimmer)
Triplet state lifetime shortened by oxygen
(20 msec if none; 0.1 usec if oxygen present)

## Slide 30: Fitting with Correct Model

## Slide 31: Fitting with Correct Model
Schwille and Haustein 2004

## Slide 32: Work Flow for FCS
<I>
I(t)
t
dI(t)
1
2
3
Principle steps
Measuring fluctuation intensities
Calculating correlation function
Fitting to biophysical model
AC: compare signal w/ itself
CC: compare signal w/ another
wr2
4td,i
D=
Diffusion coefficient:

## Slide 33: FCS also benefits from FLIM (Fluorescence Lifetime Imaging Microscopy)
FCS measurements at single point allow kinetic and diffusion properties, concentration and aggregation state of fluorescently labeled molecules to be determined.
FLIM measurement of fluorescent lifetime of fluorophore is sensitive to the molecular environment of that fluorophore.
FCS and FLIM allow information to be gathered on diffusional mobility, protein clustering and interactions, and molecular environment.
Notes: Breusegem, S.Y., Levi, M., Barry, N.P., 2006. Fluorescence Correlation Spectroscopy and Fluorescence Lifetime Imaging Microscopy. Nephron Experimental Nephrology 103, e41-e49.

## Slide 34: Fluorescence Lifetime Imaging Microscopy (FLIM)
Measure spatial distribution of differences in the timing of fluorescence excitation of fluorophores
Combines microscopy with fluorescence spectroscopy
Fluorescent lifetimes very short (ns) so need fast excitation and/or fast detectors
Requirements for FLIM instruments
  Excitation light intensity modulated or pulsed
  Emitted fluorescence measured time resolved
Notes: FLIM has its roots in two fields of research: 1) microscopy and 2) fluorescence spectroscopy. In the latter field of research, non-spatially-resolved fluorescence lifetime measurements were performed since 1926 [1], i.e. long before FLIM was developed. Typically, bulk measurements were carried out using cuvettes. Not surprisingly, most of the methodology and nomenclature used in FLIM today, e.g.‘frequency-domain’, and ‘time-domain’, have their origins in instruments that were used for cuvette-based lifetime measurements.
van Munster, E., Gadella, T.J., 2005. Fluorescence Lifetime Imaging Microscopy (FLIM), in: Rietdorf, J. (Ed.), Microscopy Techniques. Springer Berlin Heidelberg, pp. 143-175.

## Slide 35
4nsec
0.8 emitted
fluorescence
ISC
~0.03
Excited triplet
state
Phosphorescence
(μsec - msec)
Triplet state is long lived.
Fluorescence Lifetime Imaging Microscopy (FLIM)

## Slide 36: Fluorescence Lifetime Imaging Microscopy (FLIM)
Two methods for FLIM
  Frequency-domain
    Intensity of excitation light continuously modulated
    For emission measure phase shift & decrease in modulation
  Time-domain
    Pulsed excitation that is faster than fluorescence lifetime
    Emission measurement is time-resolved
Notes: The first instrument combining time resolved fluorescence spectroscopy with microscopy, dates back to 1959 [2]. In this instrument, only single point measurements could be done, so strictly speaking no actual imaging was done. The first instrument measuring spatially resolved lifetimes was described in 1989 [3]. Due to the requirement of short light pulses and fast detection, time-domain measurements became possible only about 40 years later than frequency-domain measurements using a flashlamp as excitation source [16].
van Munster, E., Gadella, T.J., 2005. Fluorescence Lifetime Imaging Microscopy (FLIM), in: Rietdorf, J. (Ed.), Microscopy Techniques. Springer Berlin Heidelberg, pp. 143-175.

## Slide 37: Fluorescence Cross-Correlation Spectroscopy
Cross-Correlation uses spectrally separable fluorophores to probe for interaction
Cross Correlation Curve Amplitude directly relates to interaction
Photon Burst Ch.1
Photon Burst Ch.2
Notes: FCCS is not too much different than single color FCS. FCCS is used to observe interaction and is much more sensitive that using differing diffusion times in single color FCS. Instead of making a “copy” signal you have two signals. The signals are then correlated together and the resulting curve gives you information about particle interaction.

## Slide 38: Cross Correlation Reveals Details of Particle Binding
Autocorrelation reveals portion of unbound particles
Cross correlation reveals bound portion
Binding constant can be calculated

## Slide 39: Controls Provide a Basis for Comparison for Cross-Correlation
Spectral cross talk can lead to false cross-correlation
With dual excitation lasers and differing expression levels, cross-correlation is never “perfect”
Controls needed for Comparison
Slaughter et al, PNAS. 2007.
Notes: Some practical considerations. Need good spectral separation, eGFP-mCherry work fine, but have some bleed through. Too much bleed through can give a high amount of false cross-correlation. With 2-color one photon FCCS the overlap for both excitation lasers is not perfect. That is to say, a 488 laser will have a smaller PSF than the 561nm laser. This results in cross-correlation standards giving results that are not “perfect.” If perfect the cross correlation curve will overlap the two auto-correlation curves. Need controls!
http://www.pnas.org/content/104/51/20320.full

## Slide 40: Fluctuations Carry the Information
Measured intensity fluctuations reflects (mobile fraction only)
  Number of particles
    concentration
  Diffusion of particles
    interaction
  Brightness
    Oligomerization
A particle that transits the confocal volume will generate groups of pulses.
  The correlation function calculates the mean duration time t of these groups.
  The variance/histogram of the signal yields information about oligomeric state
<I(t)>
dI(t)
dI(t)
FCS
PCH
Notes: The principle of FCS is being able to observe one or a few fluorescent particles enter and leave a small illuminated volume. If the sample, solution or cell, has a high concentration of tagged molecules it becomes hard to observe the needed fluctuations. I generally give the analogy of a crowded lecture hall. If the lecture hall is crowded and you were observing the lecture hall you would be less apt to notice if some one entered or left the room (i.e. a small fluctuation from the mean number of people in the hall). If only a few people were in the hall, then if someone left it would be very easy to notice (i.e. a large fluctuation from the mean number of people in the hall). This is why a large immobile population is not good for FCS. Fluctuations about the mean intensity is the information used for all FFS techniques.

## Slide 41: Photon Counting Histogram
Photon count distribution originates from a convolution of two sources
  Photon Detection Statistics
    Poisson
  Particle Number Fluctuations
    Poisson
Further complications come from variations in PSF
Information Gained
  Concentration
  Brightness
(Qian and Elson, 1989, Applied Polymer Symposia. John Wiley and Sons, New York. 305-314,1990; Chen et al, 1999 Biophys J. 77: 553–567.; Muller et al, 2000 Biophys J 78:474–486).
Photon Counts
frequency
(en=1.0)
(en=2.2)
(en=3.7)
Increasing Brightness

## Slide 42: Brightness Reveals Oligomerization
Slaughter et al, PloS ONE. 2008.

## Slide 43: Zeiss ConfoCor3: FCS Setup on a Laser Scanning Confocal Microscope
Schwille and Haustein 2004
Avalanche Photodiode Detector (APD)
Single Photon Sensitivity
Focus to tiny volume (<1 femtoliter)
Notes: http://hamamatsu.magnet.fsu.edu/articles/avalanche.html
http://www.photonics.com/EDU/Handbook.aspx?AID=25535

## Slide 44: Flip trap screen (http://www.fliptrap.org) Le Trinh et al. Gene Dev. 2011
Gene trapping vector: Citrine (YFP) flanked by splice acceptor & donor, forward orientation; mCherry (RFP) polyadenylation signal, reverse orientation; lox & FRT sites
Transposon based gene trapping technology (Tol2)
Notes: Visualize proteome via fluorescent tagging of full-length endogenous proteins
Flip trap screen done in the laboratories of Scott Fraser and Marianne Bronner at Caltech published in 2011

## Slide 45: Flip Trap Screen Labels Endogenous Proteins: Different Sub-Cellular Compartments and Cell Types

## Slide 46: Nucleus has Distinct Structural and Functional Compartments
Lanctot, C., T. Cheutin, et al. (2007). "Dynamic genome architecture in the nuclear space: regulation of gene expression in three dimensions." Nat Rev Genet 8(2): 104-115.

## Slide 50
Lanctot, C., T. Cheutin, et al. (2007). Nat Rev Genet 8(2): 104-115.

## Slide 51
http://blog.biotek.com/2010/04/sbs-2010-conference-epigenetics.html

## Slide 52: FCS Detects Intracellular Variations

## Slide 53: Diffusion Coefficients Similar to those Obtained Using FRAP
Cavey, M., Rauzi, M., Lenne, P. F. and Lecuit, T. (2008). Nature 453, 751-6.

## Slide 54: Epithelial transitions during pharyngeal pouch formation
Wnt signaling role in pharyngeal pouch formation
Adherens junction
Choe Chong P, Collazo A, Trinh Le A, Pan L, Moens Cecilia B, Crump JG (2013) Wnt-Dependent Epithelial Transitions Drive Pharyngeal Pouch Formation. Developmental Cell 24: 296-309.

## Slide 55: Alcama immunoglobulin-domain protein functions to restabilize adherens junctions
Use α-Catenin protein labeled transgenic zebrafish line to study protein mobility at adherens junction.
Alcama associates with α-Catenin at adherens junction
At transitional stage endodermal epithelium is destabilized

## Slide 56: Published FCS Studies in Zebrafish Have Used Exogenously Expressed Proteins
Proteins acting as morphogen
  Yu, S. R., M. Burkhardt, et al. (2009). Nature 461(7263): 533-536.
Receptor ligand interactions
  Ries, J., S. R. Yu, et al. (2009). Nat Methods 6(9): 643-645.

## Slide 57: Less Gnb2 in Hair Cells than Neurons

## Slide 59: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?

## Slide 60: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?
  But 100x the mass only 1/3 reduction.

## Slide 61: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?
  But 100x the mass only 1/3 reduction.
More likely causing interactions with cytoskeleton, organelles or other structures
Nucleus
Cell Membrane
Mitochondria

## Slide 62: Conclusion of examples
FCS + Flip Trap lines provide unique insights into protein kinetics in vivo.
    Intracellular differences across subcellular regions
    Developmental transitions in protein kinetics
Endogenous protein concentrations crucial for accurate FCS measurements

## Slide 63: Fluorescence Fluctuation Spectroscopy (FFS)
Bacia et al., Nature Methods 2006
wr2
4td,i
D=
Diffusion coefficient:
Notes: Bacia, K., Kim, S.A., Schwille, P., 2006. Fluorescence cross-correlation spectroscopy in living cells. Nat Methods 3, 83-89.

## Slide 64: Fluorescent recovery after photobleaching (FRAP)
Like FCS also used for calculating diffusion
Fluorescence Loss in Photobleaching (FLIP) related technique
Primary use of FLIP is to determine continuity of membranous organelles.
wr2
4td,i
D=
Diffusion coefficient:
Notes: The major difference between these two microscopy techniques is that FRAP involves the study of a cell’s ability to recover after a single photobleaching event whereas FLIP involves the study of how the loss of fluorescence spreads throughout the cell after multiple photobleaching events. This difference in purpose also leads to a difference in what parts of the cell are observed. In FRAP, the area that is actually photobleached is the area of interest. Conversely, in FLIP, the region of interest is just outside the region that is being photobleached. Another important difference is that in FRAP, there is a single photobleaching event and a recovery period to observe how well fluorophores move back to the bleached site. However, in FLIP, multiple photobleaching events occur to prevent the return of unbleached fluorophores to the bleaching region.
http://en.wikipedia.org/wiki/Fluorescence_loss_in_photobleaching
http://en.wikipedia.org/wiki/Fluorescence_recovery_after_photobleaching
http://www.olympusconfocal.com/applications/flipandfrap.html
"Frap diagram" by MDougM - Own work. Licensed under Public Domain via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Frap_diagram.svg#mediaviewer/File:Frap_diagram.svg
"Fluorescence Loss in Photobleaching Schematic" by Steven Lentz - was sent to me personally. Licensed under CC BY-SA 3.0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Fluorescence_Loss_in_Photobleaching_Schematic.jpg#mediaviewer/File:Fluorescence_Loss_in_Photobleaching_Schematic.jpg

## Slide 65: Two-Photon microscopy: Good for FRAP?
Optical sectioning by non-linear absorbance
Notes: While FRAP has been around for a while what development really made this technique take off?

## Slide 66: FRAP has been around since 1976
Again developed by Watt Webb’s laboratory at Cornell
Though it’s been around for a while can you guess what development really made FRAP take off?
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 67: Green Fluorescent Protein
From marine invertebrate, Crystal jelly (Aequorea Victoria)
Can be coded in genes and made by the organism

## Slide 68: Fluorescence Fluctuation Spectroscopy (FFS)
Fluorescence Correlation Spectroscopy (FCS)
Photon Counting Histogram (PCH)
Fluorescence Cross-Correlation Spectroscopy (FCCS)
  FCS with more than 1 color
Advantages over FRAP and FRET

## Slide 69: Fluorescence Fluctuation Spectroscopy (FFS)
Advantages over FRAP and FRET
Table: http://www.fcsxpert.com/

## Slide 70: But what do you do when FRAP and FCS give different results?
Drosophila bicoid protein gradient
With FRAP measured D=0.3 μm2/second
With FCS measured D=∼7 μm2/second
Which result do you believe?
Notes: http://www.sciencedirect.com/science/article/pii/S0092867407006630
Wieschaus Cell paper
http://www.ncbi.nlm.nih.gov/pmc/articles/PMC2920644/
FCS paper
Development paper by Wieschaus reviewing his result
http://dev.biologists.org/content/137/14/2253.full
Schematic of the Bicoid gradient in the syncytial Drosophila embryo. (A-G) Bicoid, as a transcription factor, accumulates within nuclei during interphase. The nuclear Bicoid gradient, which decreases in concentration with distance from the anterior pole, forms in less than 3 hours in a Drosophila embryo that is ~500 μm long (AP axis) and can be observed (B) before nuclei migrate to the surface of the embryo. During the first ~80 minutes (corresponding to cell cycles 1-8), nuclei proliferate in the centre of the embryo (A-C), and then migrate to the surface of the embryo in cycle 9. During the last five cell cycles, nuclei divide at the surface of the embryo (D,E). Nuclei replicate every ~9 minutes during the first nine cell cycles, but this slows to ~20 minutes in cycle 13. Nuclei are ~10 μm in diameter in pre-cycle 14 embryos (A-D) but ~6 μm in cycle 14 (E). The extent to which the mRNA encoding Bicoid, which is initially tightly localised to the anterior pole (A), becomes delocalised is a matter of controversy. Two alternative bicoid RNA distributions during cycle 14 are shown in E and F. (G) Illustration of the nucleus and surrounding cytoplasm. (H) In species that produce larger or smaller eggs than Drosophila melanogaster, the Bicoid gradient scales with egg length.

## Slide 71: Homework 5
Early on during zebrafish development, many molecules are involved in patterning the embryo’s tissues and axes. One possible explanation for this complex patterning is Alan Turing’s reaction-diffusion model. To test this you have fluorescently tagged three proteins involved in this process. Your hypothesis is that one protein acts at a long distance while another acts at a short distance and the third at an intermediate distance.
Questions: What fluorescent technique would you use to determine the mobility of these three proteins? What would you predict is the relative mobility of these three proteins?