## Slide 1: Biology 227: Methods in Modern Microscopy
Andres Collazo, Director Biological Imaging Facility
Steven Wilbert, Graduate Student, TA
Week 5 Fluorescent Correlation Spectroscopy (FCS) vs Fluorescent recovery after photobleaching (FRAP)

## Slide 2: Fluorescence correlation spectroscopy (FCS)
In 1972 Watt Webb’s laboratory at Cornell put fluorescence microscopy to new use
Studied reaction kinetics
Ethidium bromide binding to DNA
  Individually don’t fluoresce but together glow under UV
Could detect single molecules but could not repeatedly detect the same molecule
Notes: http://www.nature.com/milestones/milelight/full/milelight10.html
1990 invented two photon confocal microscopy

## Slide 3: Fluorescent recovery after photobleaching (FRAP)
FRAP has been around since 1976
Again developed by Watt Webb’s laboratory at Cornell
Unlike FCS not a single molecule technique
Looks at dynamics of populations of molecule
Though it’s been around for a while can you guess what development really made FRAP take off?
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 4: Green Fluorescent Protein
From marine invertebrate, Crystal jelly (Aequorea Victoria)
Can be coded in genes and made by the organism

## Slide 5: Techniques for studying molecular diffusion
Fluorescence correlation spectroscopy (FCS)
Fluorescent recovery after photobleaching (FRAP)
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 6: Techniques for studying molecular diffusion
Fluorescence correlation spectroscopy (FCS)
Fluorescent recovery after photobleaching (FRAP)
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 7: Fluorescence Fluctuation Spectroscopy (FFS)
Fluorescence Correlation Spectroscopy (FCS)
Photon Counting Histogram (PCH)
Fluorescence Cross-Correlation Spectroscopy (FCCS)
  FCS with more than 1 color

## Slide 8: Fluorescence Fluctuation Spectroscopy (FFS)
Causes of fluctuations
Diffusion of labeled molecules due to Brownian motion
  In cells wide range of things cause movement (cellular trafficking, protein interaction etc.)
Photophysical processes of labeled molecules

## Slide 9: Fluctuations Carry the Information
Measured intensity fluctuations reflects (mobile fraction only)
  Number of particles
    concentration
  Diffusion of particles
    interaction
  Brightness
    Oligomerization
A particle that transits the confocal volume will generate groups of pulses.
  The correlation function calculates the mean duration time t of these groups.
  The variance/histogram of the signal yields information about oligomeric state
<I(t)>
dI(t)
dI(t)
FCS
PCH
Notes: The principle of FCS is being able to observe one or a few fluorescent particles enter and leave a small illuminated volume. If the sample, solution or cell, has a high concentration of tagged molecules it becomes hard to observe the needed fluctuations. I generally give the analogy of a crowded lecture hall. If the lecture hall is crowded and you were observing the lecture hall you would be less apt to notice if some one entered or left the room (i.e. a small fluctuation from the mean number of people in the hall). If only a few people were in the hall, then if someone left it would be very easy to notice (i.e. a large fluctuation from the mean number of people in the hall). This is why a large immobile population is not good for FCS. Fluctuations about the mean intensity is the information used for all FFS techniques.

## Slide 10: Creating the Autocorrelation Function
“Copy” signal
Photon Burst
dI(t)
dI(t+t)
t=0
t=tD
t=inf
Notes: The fluctuations generated can be analyzed in many ways. FCS relies on the auto-correlation function which is a signal processing technique. The autocorrelation compares a signal against itself. In this case, a particle enters the focal volume and generates a photon burst. The collected signal is “copied” and the two copies are compared against one another as you shift the “copy” in time. The copy signal is shifted by some amount of time given by the greek symbol tau. All data analysis will be done in reference to the shift time tau.

## Slide 11: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 12: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 13: Autocorrelation Yields Diffusion and Concentration
Fit Autocorrelation curve for Diffusion time (tD) and particle concentration N
Notes: The larger the particle, the longer it will take to transverse the focal volume thus the photon burst will be longer in time. This results in the correlation function moving the left for larger particles. The diffusion time gives information about the diffusion coefficient, the molecular weight and possibly the viscosity of the media. The correlation curve amplitude is inversely proportional to the particle concentration. The concentration, N, is the average number of molecules in the focal volume at one time. Standard dye solutions with known diffusion coefficients can be used to characterize the focal volume. Once that is done, you can use the focal volume information and the Number of particles to get an accurate measure of the MOBILE concentration (mol/L). The curve amplitude being inversely proportional to the particle number makes sense because the higher the N, the smaller the fluctuations will be from the mean intensity giving less correlation.
ALL DATA IS FIT USING A NON-LINEAR LEAST SQUARES ERRORS FUNCTION TO GET DIFFUSION TIMES AND N. You will run the risk of getting bad results with bad curve fitting or curve fitting interpretation.

## Slide 14: Fitting with Correct Model
Schwille and Haustein 2004

## Slide 15: Work Flow for FCS
Principle steps
Measuring fluctuation intensities
Calculating correlation function
Fitting to biophysical model
wr2
4td,i
D=
Diffusion coefficient:
Gnb2 in Hair Cells
G(t)=1+Gt(t)*Gd(t)
Autocorrelation function:
Gt(t)=1+
Tb*e-t/tb
1-Tb
Blinking correlation:
Gd(t)=
ΦI
td,i
1+
t
aI
ed1
td,i
1+
t
aI
ed2
*
1
S
0.5
*
Translational correlation:
1
2
3

## Slide 16: Work Flow for FCS
Principle steps
Measuring fluctuation intensities
Calculating correlation function
Fitting to biophysical model
wr2
4td,i
D=
Diffusion coefficient:
Gnb2 in Hair Cells
G(t)=1+Gt(t)*Gd(t)
Autocorrelation function:
1
2
3

## Slide 17: Zeiss LSM 880: FCS Setup on a Laser Scanning Confocal Microscope
Schwille and Haustein 2004
Gallium arsenide phosphide (GaAsp) detectors
Single Photon Sensitivity
Focus to tiny volume (<1 femtoliter)
Notes: http://www.photonics.com/EDU/Handbook.aspx?AID=25535

## Slide 18: Fluorescence Fluctuation Spectroscopy (FFS)
Bacia et al., Nature Methods 2006
wr2
4td,i
D=
Diffusion coefficient:
Notes: Bacia, K., Kim, S.A., Schwille, P., 2006. Fluorescence cross-correlation spectroscopy in living cells. Nat Methods 3, 83-89.

## Slide 19: Techniques for studying molecular diffusion
Fluorescence correlation spectroscopy (FCS)
Fluorescent recovery after photobleaching (FRAP)
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 20: Fluorescent recovery after photobleaching (FRAP)
Like FCS also used for calculating diffusion
Fluorescence Loss in Photobleaching (FLIP) related technique
Primary use of FLIP is to determine continuity of membranous organelles.
wr2
4td,i
D=
Diffusion coefficient:
Notes: The major difference between these two microscopy techniques is that FRAP involves the study of a cell’s ability to recover after a single photobleaching event whereas FLIP involves the study of how the loss of fluorescence spreads throughout the cell after multiple photobleaching events. This difference in purpose also leads to a difference in what parts of the cell are observed. In FRAP, the area that is actually photobleached is the area of interest. Conversely, in FLIP, the region of interest is just outside the region that is being photobleached. Another important difference is that in FRAP, there is a single photobleaching event and a recovery period to observe how well fluorophores move back to the bleached site. However, in FLIP, multiple photobleaching events occur to prevent the return of unbleached fluorophores to the bleaching region.
http://en.wikipedia.org/wiki/Fluorescence_loss_in_photobleaching
http://en.wikipedia.org/wiki/Fluorescence_recovery_after_photobleaching
http://www.olympusconfocal.com/applications/flipandfrap.html
"Frap diagram" by MDougM - Own work. Licensed under Public Domain via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Frap_diagram.svg#mediaviewer/File:Frap_diagram.svg
"Fluorescence Loss in Photobleaching Schematic" by Steven Lentz - was sent to me personally. Licensed under CC BY-SA 3.0 via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Fluorescence_Loss_in_Photobleaching_Schematic.jpg#mediaviewer/File:Fluorescence_Loss_in_Photobleaching_Schematic.jpg

## Slide 21: Fluorescent recovery after photobleaching (FRAP)
Instructions on class web site from Alex Webster.
From publication: Wachsmuth, M., 2014. Molecular diffusion and binding analyzed with FRAP. Protoplasma 251, 373-382.
Note the bleach region in blue. Use this long thin rectangle.
Figure 3 from Wachsmuth paper.
Notes: Evaluating a FRAP experiment. a Prebleach and post-bleach
images of a FRAP experiment of a nuclear protein with the bleach ROI
(“bl”, blue), a ROI for background signal (“bg”, green), a ROI for the total
signal from the bleached cell (“tot”, yellow), and a ROI for signal from a
reference cell (“ref”, red). bTypical relative durations of prebleach, bleach
pulse, and post-bleach sequence. c The averaged fluorescence intensities
from the ROIs shown in (b) versus time; time zero corresponds to the first
post-bleach image. d Intensities “bl,” “ref,” and “tot” from (c) after
background correction. e Intensity “bl” from (d) normalized to “tot” or
“ref” from (d). f Intensity “bl” from (e) normalized to the prebleach
intensity. gBleach ROI of area Aand simplemodel of diffusivemolecules

## Slide 22: Two-Photon microscopy: Good for FRAP?
Optical sectioning by non-linear absorbance
Notes: While FRAP has been around for a while what development really made this technique take off?

## Slide 23: Techniques for studying molecular diffusion
Fluorescence correlation spectroscopy (FCS)
Fluorescent recovery after photobleaching (FRAP)
Table: http://www.fcsxpert.com/
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 24: But what do you do when FRAP and FCS give different results?
Drosophila bicoid protein gradient
With FRAP measured D=0.3 μm2/second
With FCS measured D=∼7 μm2/second
Which result do you believe?
Notes: http://www.sciencedirect.com/science/article/pii/S0092867407006630
Wieschaus Cell paper
http://www.ncbi.nlm.nih.gov/pmc/articles/PMC2920644/
FCS paper
Development paper by Wieschaus reviewing his result
http://dev.biologists.org/content/137/14/2253.full
Schematic of the Bicoid gradient in the syncytial Drosophila embryo. (A-G) Bicoid, as a transcription factor, accumulates within nuclei during interphase. The nuclear Bicoid gradient, which decreases in concentration with distance from the anterior pole, forms in less than 3 hours in a Drosophila embryo that is ~500 μm long (AP axis) and can be observed (B) before nuclei migrate to the surface of the embryo. During the first ~80 minutes (corresponding to cell cycles 1-8), nuclei proliferate in the centre of the embryo (A-C), and then migrate to the surface of the embryo in cycle 9. During the last five cell cycles, nuclei divide at the surface of the embryo (D,E). Nuclei replicate every ~9 minutes during the first nine cell cycles, but this slows to ~20 minutes in cycle 13. Nuclei are ~10 μm in diameter in pre-cycle 14 embryos (A-D) but ~6 μm in cycle 14 (E). The extent to which the mRNA encoding Bicoid, which is initially tightly localised to the anterior pole (A), becomes delocalised is a matter of controversy. Two alternative bicoid RNA distributions during cycle 14 are shown in E and F. (G) Illustration of the nucleus and surrounding cytoplasm. (H) In species that produce larger or smaller eggs than Drosophila melanogaster, the Bicoid gradient scales with egg length.

## Slide 25: Do FRAP and FCS give different results?
You will do the experiment in same cell type
Recent paper did this experiment:
  Macháň, R., Foo, Yong H., Wohland, T., 2016. On the Equivalence of FCS and FRAP: Simultaneous Lipid Membrane Measurements. Biophysical Journal 111, 152-161.
Paper presents a hypothesis for why these techniques sometimes give different results
Notes: Macháň, R., Foo, Yong H., Wohland, T., 2016. On the Equivalence of FCS and FRAP: Simultaneous Lipid Membrane Measurements. Biophysical Journal 111, 152-161.
Bleaching correction

## Slide 26: Techniques for studying molecular diffusion
Fluorescence correlation spectroscopy (FCS)
Fluorescent recovery after photobleaching (FRAP)
Notes: http://www.ncbi.nlm.nih.gov/pmc/articles/PMC1334945/

## Slide 27: Meeting Summary on Impact of Genomics on Drug Discovery and Development
Rastan, S. (2001). Genomics: saviour or millstone? Trends in Genetics 17, 247-248.
Genome (What could happen)
Transcriptome (What might be happening)
Proteome (What is happening)
Lucitt, M. B., et al. (2008). Analysis of the Zebrafish Proteome during Embryonic Development. Molecular & Cellular Proteomics 7, 981-994.
Levi, L., et al. (2009). Revealing genes associated with vitellogenesis in the liver of the zebrafish (Danio rerio) by transcriptome profiling. BMC Genomics 10, 141.

## Slide 28: Flip trap screen (http://www.fliptrap.org) Le Trinh et al. Gene Dev. 2011
Gene trapping vector: Citrine (YFP) flanked by splice acceptor & donor, forward orientation; mCherry (RFP) polyadenylation signal, reverse orientation; lox & FRT sites
Transposon based gene trapping technology (Tol2)
Notes: Visualize proteome via fluorescent tagging of full-length endogenous proteins
Flip trap screen done in the laboratories of Scott Fraser and Marianne Bronner at Caltech published in 2011

## Slide 29: Flip Trap Screen Labels Endogenous Proteins: Different Sub-Cellular Compartments and Cell Types
Cell Membrane
Nuclei
α- Catenin
Hmga2
Rbms3
Rab3ab
Cytoplasm
Zebrafish Ear Development
Cytoplasm+Nuclei
1 day
2 days
3-4 days
FM1-43
memCherry
memCherry
Hmga2

## Slide 30: Nucleus has Distinct Structural and Functional Compartments
Lanctot, C., T. Cheutin, et al. (2007). "Dynamic genome architecture in the nuclear space: regulation of gene expression in three dimensions." Nat Rev Genet 8(2): 104-115.

## Slide 31
FCS + Ubiquitously Expressed Proteins Can Reveal Hidden Variations
D
A
High Mobility Group AT-Hook 2 (Hmga2)
transcription
Hmga2
Expressed in all nuclei
Part of transcriptional complex
Down-regulated in hair cells
SA
SD
pA
mCherry
citrine
citrine
AT-hook

## Slide 32
27 hpf
D
A
30 hpf
D
A
Z-Proj
snRNP
5’
3’
spliceosome
complex
SLU7
Different nuclear compartment than Hmga2
Part of pre-mRNA spliceosome complex
Also down-regulated in hair cells
SA
SD
pA
mCherry
citrine
citrine
Znf
Synergistic Lethal with U5 snRNA 7 (Slu7) Another Ubiquitously Expressed Nuclear Protein

## Slide 33
In Vivo Readout of Transcriptional Activity:
Faster Mobility in Dorsal Roof Cells
Gt(slu7-citrine)ct94a
Diffusion Coeff. (mm2/sec)
hair-
cells
support
cells
canal
apex
dorsal
roof
N=39
N=8
N=8
N=8
P=3.1x10-3
N=16
canal
base
Diffusion Coeff. (mm2/sec)
hair
cells
support
cells
canal
cells
dorsal
roof
N=24
N=22
N=13
N=11
P=4.3 x10-3
P=2.4x10-3
Gt(hmga2-citrine)ct29a
55 hpf
48 hpf
76 hpf

## Slide 34
Developmental Stage Dependent Decrease of Histone (H2B) Mobility in Dorsal Roof Cells
Diffusion Coeff. (mm2/sec)
support
cells
dorsal
roof
N=17
N=18
N=12
N=20
P=6.9x10-3
H2B mobility at 50hpf
Diffusion Coeff. (mm2/sec)
support
cells
dorsal
roof
N=23
N=8
N=16
P=0.19
H2B mobility at 30hpf
faster diffusion of histone at transcription site
Hmga2
Slu7
inactive chromatin
snRNP
5’
3’
SLU7
Model
hair
cells
canal
cells
hair
cells
Lanctot, C., T. Cheutin, et al. (2007). Nat Rev Genet 8(2): 104-115.

## Slide 35: In Vivo Readout of Transcriptional Activity: Trichostatin A (TSA) treatment Slows Hmga2 Protein Diffusion
TSA pharmacological inhibitor of Histone Deacetylase (HDAC)
Hmga2 slowed both dorsal and ventral versus DMSO control
P=5.7x10-4
N=29
N=26
http://blog.biotek.com/2010/04/sbs-2010-conference-epigenetics.html
N=28
N=32
P=0.006

## Slide 36: FCS Detects Intracellular Variations
α-Catenin time-lapse beginning 26 hpf
Time-lapse 16 hrs, 50 min
Expressed in cell membranes
Concentrated in sensory organs; apical.
D
A

## Slide 37: Diffusion Coefficients Similar to those Obtained Using FRAP
N=31
N=30
N=32
P= 0.00094
P= 1.23 x 10-5
E-Cadherin: Published FRAP measurements
Spot Adherens Junctions (SAJ),
Drosophila embryonic epithelium
0.06 Highest; 0.005 Lowest (mm2/sec)
Cavey, M., Rauzi, M., Lenne, P. F. and Lecuit, T. (2008). Nature 453, 751-6.
30 hpf
Hair Cells
Epidermis
α-Catenin

## Slide 38: Epithelial transitions during pharyngeal pouch formation
Wnt signaling role in pharyngeal pouch formation
Adherens junction
Choe Chong P, Collazo A, Trinh Le A, Pan L, Moens Cecilia B, Crump JG (2013) Wnt-Dependent Epithelial Transitions Drive Pharyngeal Pouch Formation. Developmental Cell 24: 296-309.

## Slide 39: Alcama immunoglobulin-domain protein functions to restabilize adherens junctions
Use α-Catenin protein labeled transgenic zebrafish line to study protein mobility at adherens junction.
Alcama associates with α-Catenin at adherens junction
At transitional stage endodermal epithelium is destabilized

## Slide 40: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?

## Slide 41: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?
  But 100x the mass only 1/3 reduction.

## Slide 42: What Do Differences in Diffusion Coefficients Mean?
Binding to larger protein?
  But 100x the mass only 1/3 reduction.
More likely causing interactions with cytoskeleton, organelles or other structures
Nucleus
Cell Membrane
Mitochondria