## Slide 1: Camera Status
Charles Sommer – Serena Ferraro – Thibaud Talon
October 21st, 2019

## Slide 2: Status
Vibration tested (?)
Flight pieces are manufactured
EM of electronic boards + optical sensors were TVAC
  5 cycles of -15 to 45C
Base software fully coded
  CAN control
  Low level drivers

## Slide 3: Open issues and solutions
Science camera has heating issues
  Overheats in vacuum
  Operating temperature range is limited: 0 to 50 degrees C
  Designed heat dissipation + heating solutions
  Already re-designed electronics to host heater
Science camera and Boom Inspection camera are the same
  Will cover it by adding black anodized aluminum around it
Temperature sensors were not working correctly
  Switched to thermistors and changed electronics

## Slide 4: Science camera thermal
Add 100um thermal pad
at the bottom of the box
Buy new MU9PM, board level
Reuse or buy new camera box
Add heater film
around casing
Add 1mm thermal pad
between box and bracket

## Slide 5: Boom inspection camera thermal
Surround camera with black
anodized aluminum + add
dissipation

## Slide 6: Upcoming steps
Solder new version of camera electronics
Replace Science Camera
Manufacture surroundings for Boom Inspection Camera
TVAC camera electronics with heater + thermistors + dissipators