## Slide 1: Radio Interface Board Status
Corentin Lubeigt
October 22st, 2019

## Slide 2: Overview
Board between the Central Stack and Radio + Transponder stack
Functionalities:
  Convert VBAT (direct from battery) to 12V for the Radio
  Convert VBAT to 5V (with on/off feature) to 5V for the Transponder
  Current and voltage sensing of 12V and 5V with a I2C ADC
  Forward data signals (CAN for Transponder, UART for Radio)
  Process and forward Firecode generated by Radio to the EPS

## Slide 4: Status
Version 2.1 soldered, tested through TVAC
Radio powered with the Radio IFB in the middle

## Slide 5: Open issues and solutions
Problem on 5V lines: 5V is shared by MirrorSat, PIC and MirrorBox. The two last are microcontroller and cannot stand a too low input voltage. When current drawn increases, we observe voltage drop.
  Test different switches to pick the most efficient one to minimize voltage drop through the board
  Cable analysis and design to estimate the voltage drop (through Central IFB to Y IFB harness and and through Y IFB to MirrorBox harness)

## Slide 6: Forthcoming steps
Solder new IFB when it comes in
Functional test with actual cable length
TVAC final version of IFB
Integrate to FlatSat
Order FM boards

## Slide 7: +/-Y Interface Boards Status
Corentin Lubeigt
October 22st, 2019

## Slide 8: Overview
Board between the Central Stack and Solar Panels, MirrorBox, the Payload Interface Computer and its electromagnet boards
Functionalities:
  Provide 5V switched to PIC, MirrorBox and MirrorSat (this one isolated)
  Generate UART from I2C to talk to the MirrorBox
  On-board temperature sensing
  Interface with Solar Panels, ADCS (coarse sun sensor) and EPS (ACU)
  Burnwires mechanism for antenna deployment

## Slide 10: Status
Version 6.4 soldered and tested
  Most of the board passed save the 5V lines (see next slide)
Next version (v7.x) ordered
-Y interface board serve as a EM for the +Y interface board

## Slide 11: Open issues and solutions
Problem on 5V lines: 5V is shared by MirrorSat, PIC and MirrorBox. The two last are microcontroller and cannot stand a too low input voltage. When current drawn increases, we observe voltage drop.
  Test different switches to pick the most efficient one to minimize voltage drop through the board
  Cable analysis and design to estimate the voltage drop (through Central IFB to Y IFB harness and and through Y IFB to MirrorBox harness)

## Slide 12: Forthcoming steps
Solder new IFB when it comes in
Functional test with actual cable length
TVAC final version of IFB
Integrate to FlatSat
Order FM boards

## Slide 13: Central Interface Board Status
Fabien Royer - Charles Sommer – Corentin Lubeigt – Thibaud Talon
October 22st, 2019

## Slide 14: Overview
4 layers board in central stack:
  Top layer: data and low power lines
  Middle top layer: high power lines
  Middle bottom layer: ground
  Bottom layer: data and low power lines
Functionalities:

## Slide 15: Status
Received first version of the board and components

## Slide 16: Open issues and solutions
So far no issues detected

## Slide 17: Forthcoming steps
Solder components on board
Perform functional test on board

## Slide 18: Flight Preparation Panel Board Status
Corentin Lubeigt
October 22st, 2019

## Slide 19: Overview
Board meant to access the Central stack PC104 from the outside of the spacecraft. It is the main interface between test engineer and the spacecraft
Functionalities: route all the PC104 lines from the PC104 of the central stack the outside of the spacecraft
  Data lines to be monitored (UARTs, I2Cs, CAN, SPI, GPIOs)
  Power lines from the EPS
  Probed lines from the Central IFB

## Slide 20: Status
First version ordered

## Slide 21: Open issues and solutions
No issue so far for the board has not arrived yet

## Slide 22: Forthcoming steps
Solder new IFB when it comes in
When Central stack is assembled, plug it in and let it be the only interface used for testing