## Slide 1: ConOps
Charles Sommer
October 21st, 2019

## Slide 2: ConOps – Considerations
90 min polar orbit
NORAD data retrieval 7 days after launch
Always switching to sun pointing when battery reaches 55% (43Wh) of capacity (77Wh)
Always taking night side when doing autonomous operations
Battery and Camera heaters ON when on night side
Transponder ON only when necessary and at full battery power
Worst case power losses considered
  5% from Kill Switch
  20% from EPS switches
  10%, 20% or 40% for Interface Boards switches

## Slide 3: Overview
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 4: AAReST Initialization
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 5: AAReST Initialization
 |  | Step | Actions | ADCS Mode – State | Duration
NIGHT | AUTO | Autonomous Init. | EPS + OBC + Radio ON (by default) | None – Tumbling | 30 s max
 |  |  | UHF/VHF Antennas Deployment |  | 
 |  |  | Beacon every 1 min |  | 
NIGHT | AUTO | ADCS Initial Commissioning | ADCS ON + Health check |  | 15 s
 |  |  | Angular rates determination |  | 5 min
 |  |  | Detumbling w/ torque rods | Detumbling | 4 orbits
 | AUTO | TLE & Sun Pointing | GPS ON + Signal Acquisition + TLE computation |  | 5 min
NIGHT AND DAY |  |  | Sun pointing with torque rods + battery charging | Survival – Sun Tracking | 2 orbits
 | MANUAL | ADCS Magnetometer and Reaction Wheel Commissioning | Magnetometer calibration and survey | None – Tumbling | 3 orbits
 |  |  | Deploy Magnetometer if necessary |  | 1 orbit
 |  |  | Reaction wheels ramp-up test |  | 1 orbit
NORAD
data

## Slide 6: AAReST Initialization – Energy drawn
Chart: Time elapsed (s)
| 1 | 6 | 11 | 16 | 17 | 18 | 19 | 21 | 31 | 331 | 21931 | 22242 | 22244 | 33044 | 33045 | 38445 | 54645 | 54705 | 60105 | 65505 | 70905
Remaining battery energy (Wh) | 76.9974 | 76.9846 | 76.9681 | 76.9516 | 76.9491 | 76.9465 | 76.944 | 76.9387 | 76.9123 | 76.0899 | 67.3187 | 66.4662 | 66.4607 | 77 | 77 | 76.9258 | 77 | 76.7468 | 77 | 72.6351 | 77

## Slide 7: Camera Deployment
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 8: Camera Deployment
 |  | Step | Actions | ADCS Mode – State | Duration
 | MANUAL | Camera Stage 1 Deployment | Camera ON + Health check + Download first images | Sun Tracking | 1 orbit
DAY |  |  | Actuate Camera Burnwire + Take BIC picture | Conf Change | 10 s
 | MANUAL | Camera Stage 2 Deployment | Start Camera Accelerometer acquisition + BIC video | Sun Tracking | 5 s
 |  |  | Actuate Camera Frangibolt | None – Tumbling | 20 s
 |  |  | Set new inertias + detumble + download video/data | Detumbling | 1 orbit
 | MANUAL | ADCS Fine Sun Sensor and Star Tracker Commissioning | Fine Sun Sensor Commissioning | Sun Tracking | 1 orbit min.
 |  |  | Star Tracker Commissioning | Star Tracking | 1 orbit min.

## Slide 9: Camera Deployment – Energy drawn
Chart: Time elapsed (s)
| 2 | 32 | 992 | 993 | 1013 | 1133 | 1135 | 6535 | 6537 | 6539 | 6559 | 6679 | 6681 | 6683 | 12083 | 12085 | 17485 | 17605 | 23005 | 28405 | 28410 | 28415 | 28420 | 28540 | 28545 | 28550 | 33950
Remaining battery energy (Wh) | 77 | 77 | 77 | 76.9986 | 76.9978 | 76.8197 | 76.8298 | 77 | 77 | 76.8215 | 76.636 | 76.7425 | 76.7481 | 76.7492 | 77 | 77 | 77 | 77 | 77 | 77 | 76.9998 | 76.9996 | 76.9994 | 76.8268 | 76.8361 | 76.8455 | 77

## Slide 10: Rigid Mirrors Tests
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 11: Rigid Mirrors Tests
 |  | Step | Actions | ADCS Mode – State | Duration
DAY | MANUAL | Rigid Mirror Initialization | RM ON + Health check + Release Mirror | Sun tracking | 1 min
 |  |  | Camera ON + Set picomotors ground values to MirrorBox |  | 1 min
NIGHT | AUTO | RM Test | Fine point towards calibration star | Fine pointing | 10 min
 |  |  | Take several SIC image every n seconds (star centered + boom jitter test) |  | 30 min
 |  |  | Desaturate RW + Download and assess images + recharge | RW Desaturation + Sun tracking | 1 orbit
NIGHT | AUTO | RM Blind Search Algorithm (if necessary) | Fine point towards calibration star | Fine pointing | 10 min
 |  |  | Start blind search algorithm (if necessary) + save SC images |  | 30 min
 |  |  | Desaturate RW + Download and assess images + recharge | RW Desaturation + Sun tracking | 1 orbit
NIGHT | AUTO | RM Optical Alignment | Fine point towards calibration star | Fine pointing | 10 min
 |  |  | Start optical alignment algorithm + save SC images |  | 30 min
 |  |  | Desaturate RW + Download and assess images + recharge | RW Desaturation + Sun tracking | 1 orbit

## Slide 12: Rigid Mirrors Tests – Energy drawn
Chart: Time elapsed (s)
| 2 | 4 | 34 | 44 | 46 | 51 | 56 | 656 | 661 | 841 | 843 | 845 | 2756 | 8156 | 8216 | 8336 | 8341 | 8343 | 8943 | 10743 | 10748 | 10928 | 10930 | 10932 | 11043 | 16443 | 16503 | 16743 | 16748 | 16750 | 17350 | 19150 | 19155 | 19335 | 19337 | 19339 | 20050 | 25450 | 25510 | 25750
Remaining battery energy (Wh) | 77 | 77 | 77 | 77 | 77 | 77 | 77 | 72.9369 | 72.903 | 71.6823 | 71.6752 | 71.6685 | 65.226 | 77 | 77 | 77 | 77 | 77 | 72.9369 | 60.7476 | 60.7137 | 59.493 | 59.4859 | 59.4792 | 59.105 | 77 | 77 | 77 | 77 | 77 | 72.9369 | 60.7476 | 60.7137 | 59.493 | 60.7405 | 60.7338 | 58.3368 | 77 | 77 | 77

## Slide 13: Deformable Mirrors Tests
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 14: Deformable Mirrors Tests
 |  | Step | Actions | ADCS Mode – State | Duration
 |  | MirrorSat Initialization | Power up MS + Healthcheck + downlink results | Sun tracking | 1 orbit
Same operations as RM |  |  |  |  | 
NIGHT | AUTO | DM Influence Function Computation | Fine point towards calibration star | Fine Pointing | 10 min
 |  |  | Start influence function computation algorithm + save SIC images + influence function results |  | Several orbits
 |  |  | Desaturate RW + Download and assess results + Recharge | RW Desaturation | 5 orbits
NIGHT | AUTO | DM Wavefront Error Minimization | Fine point towards calibration star | Fine Pointing | 10 min
 |  |  | Start wavefront error minimization algorithm |  | Several orbits
 |  |  | Desaturate RW + Download and assess results + Recharge | RW Desaturation | 5 orbits

## Slide 15: Deformable Mirrors Tests – Energy Drawn
Chart: Time elapsed (s)

## Slide 16: MirrorSats Reconfiguration
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 17: MirrorSats Reconfiguration
 |  | Step | Actions | ADCS Mode – State | Duration
DAY | MANUAL | MS Frangibolt Actuation | Camera, PICs, WiFi ON + Start BIC video + Actuate Frangibolt | None | 20 s
 |  |  | Detumble + download video + Verify MS still held by permanent mags | Detumble + Sun Tracking | 1 orbit
 |  | MS Free Fly Test | Start BIC video + Actuate Burnwire | None | 2 s
 |  |  | Actuate EMS to gently push MirrorSat + Test LED pattern |  | 10 s
 |  |  | Pull MirrorSat back with EMS |  | 10 s
 |  |  | Detumble + download video and results | Detumble + Sun Tracking | 1 orbit
 |  | MS Reconfiguration | Start BIC video + Actuate EMS to push MirrorSat | None | 2 s
 |  |  | Update ADCS to L shaped inertias with 1 MS attached | Conf Change | 5 s
 |  |  | Use LEDs and EMS to let MS free fly X mm away |  | 10 s
 |  |  | Rotate CoreSat 45 deg |  | 10 s
 |  |  | Pull back, dock MS back with EMS + update ADCS inertias | None | 10 s
 |  |  | Detumble + download video and results | Detumble + Sun Tracking | 1 orbit

## Slide 18: IIST MirrorSat Extended Mission
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 19: IIST MirrorSat Extended Mission
 |  | Step | Actions | ADCS Mode – State | Duration
DAY | MANUAL | IIST MirrorSat Separation | Actuate EMS to gently push away IIST MS | None | 20 s
 |  |  | Update ADCS to I shaped inertias with 1 MS missing | Conf Change | ?
 |  | IIST MirrorSat Experiment | Keep IIST MS in view of patch antenna (max 1km?) |  | ?
 |  |  | Actuate IIST MS propulsion system at a given distance (?) |  | ?

## Slide 20: MirrorSats Decommission
AAReST Initialization
Camera Deployment
Rigid Mirror 1 Test
Rigid Mirror 2 Test
Deformable Mirror 1
Narrow Test
Deformable Mirror 2
Narrow Test
Surrey MirrorSat Reconfiguration
Deformable Mirror 1
Wide Test
IIST MirrorSat Reconfiguration
Deformable Mirror 2
Wide Test
IIST MirrorSat Extended Mission
AAReST Decommission
NARROW OPERATIONS
WIDE OPERATIONS

## Slide 21: AAReST Decommission
Send a command to switch OFF:
  OBC
  Radio Controller
Radio 12V line would still be powered (unswitchable)
Currently, no “firecode” like command to switch off everything