## Slide 1: Ground Stations and Radio License
Charles Sommer
October 22nd, 2019

## Slide 2: AAReST RF System
2 bands:
  2 meters band, VHF, uplink: amateur band
  70 centimeters band, UHF, downlink: amateur band
2 radios:
  One AstroDev Helium 100 Transceiver:
    amateur radio main TM/TC transceiver, GFSK, 19.2 kbps
  One AMSAT Linear Transponder with two radios:
    amateur radio transponder
    amateur radio secondary TM/TC transceiver, FSK/BPSK, 1.2 kbps
3 antennas:
  One VHF uplink antenna shared by
  Two UHF downlink antennas

## Slide 3: Organizations
ITU: International Telecommunications Union
  Coordinates all world-wide frequencies
  Allocates spectrum internationally
FCC: Federal Communications Commission
  Regulates use of frequencies inside the US
  Issues licenses to operate US spacecraft
IARU: International Amateur Radio Union
  Coordinates amateur frequencies allocations
ARRL: American Radio Relay League
  Advocates to the FCC for amateurs
AMSAT: Radio Amateur Satellite Corporation
  US entity that promotes amateur radio in space
  NOAA: National Oceanic and Atmospheric Administration
    Remote sensing authority

## Slide 4: Amateur vs. Experimental vs. Commercial
AstroDev radio (bought in 2017) operates only on amateur bands
Using amateur bands is great to get HKTM from all over the world
ITU/IARU has said our request would be declined (May 2019)
  Too many uncoordinated CubeSats using amateur bands
  Bad practices (using amateur bands with no amateur purpose)
Need to provide amateur radio service to the community
Embedding an AMSAT Transponder

## Slide 5: Licenses
Title 47 of Code of Federal Regulations:
Part 97: Amateur Radio Service License
  Based on IARU coordination
  Need HAM license
Part 5: Experimental Radio Service License
  For ground station and spacecraft

## Slide 6: Licensing process
AAReST Team
IARU
Coordinates amateur frequencies assignments to avoid interference between satellites
1. Coordination paper
2. Freq. assignment
3. FCC folder
IARU consent / assignment
NOAA approval letter (exemption?)
Orbital debris assessment (NASA ODAR/DAS)
ITU SpaceCap analysis
ITU Cost Recovery Letter
Mission details
FCC
Analyzes and accepts license requests
Forward SpaceCap notice to ITU
4. Amateur and experimental license requests
ITU
Keeps database of frequencies in use
5. SpaceCap notice
6. Grants licenses
1 month+
2 month+
3 month+

## Slide 7: Ground Stations
University of Surrey and IIST have working and nationally registered UHF/VHF Ground Stations
  Does it work @ 19.2 kbps?
California State University Northridge has a working UHF/VHF Ground Station
  Would need to purchase 19.2 kbps radio + modem
Is 19.2 kbps okay for our licenses?
Would use Surrey’s Ground Station software in a network of GS