## Slide 1: Antenna Status
Corentin Lubeigt
October 22st, 2019

## Slide 2: Overview
Tape measure ¼ of wavelength antennas
  UHF: 436 MHz  172mm
  VHF: 144.5 MHz  512mm
Antenna system
  Two UHF antennas (one for transponder, one for transceiver)
  One VHF antenna shared by the two units (use of a Wilkinson Power Splitter)
LC network for impedance match

## Slide 3: Antenna Boards
VHF antenna shared by both transponder and radio
Radio UHF antenna
Transceiver UHF antenna

## Slide 4: Status
Deployment test done on a test structure
New assembly process
  Heat gun to solder antenna on PCB
  MGSE to assure perpendicularity between antenna and ground plane
Test with network analyzer to determine actual impedance

## Slide 5: Open issues and solutions
Actual impedance is very sensitive to manufacture
  Several flight antennas will be delivered and the best antenna will be selected

## Slide 6: Upcoming steps
Finish tests on current antennas (L-net, Wilkinson Power Splitter)
Manufacture flight antennas (three of each), tests will be done on the mass model to reproduce the actual ground plane
  Manufacture mounting parts

## Slide 7: Transceiver tests Status
Corentin Lubeigt
October 22st, 2019

## Slide 8: Brief
AstroDev Helium 100
  Amateur Radio bands
    TX: UHF band (19.2kbps)
    RX: VHF band (19.2kbps)
  Receive sensitivity: -104.7 dBm @ BER 10-3
  Power:
    12V line power: 7W
    Transmit power: ~1.35W

## Slide 9: Status
Radio tested with SDR and GNURadio
  in lab tests, transmit power < 10mW
Firecode system tested (sends a pulse when key detected)

## Slide 10: Open issues and solutions
Need to do outdoor test with the tape measure antennas
Receiver bandwidth very large (~200kHz), it may catch any AX.25 signals.
  Need to filter out signal as soon as they are received by the OBC

## Slide 11: Upcoming steps
Wire the Firecode pin to the PC104 H1 pin 3 to send it to the R-IFB
Test with EPS, R-IFB and Radio
Outdoor test with tape measure antenna